LED FLOODLIGHT INSTRUCITON

SPECIFICATION:

Model:

Voltage: 180-240V/50-60Hz

Power: 10W~100W

Degree of protection: IP65

Class of protection: I

Material: Aluminium die-casting

Colour temperature: 2700K~6500K

Luminous output: 70 lm/W

Beam angle: 120 degree

Life time: 50000 h

Easy installation and maintenance

A: Protective glass shield

B: LED light source

C: Bracket

D: Cable

E: Single Tripod

INSTALLATION:

- Perform holes according to given measurements where it’s relative to be secured for a projector

- Complete the installation by tightening base screws and select a suitable position.

- Turn on the power.

CAUTION:

- Please read the instruction carefully before installation and preserve it well.

- Must be installed and assembled by a qualified electrician.

- Before installation, please be sure to cut off the main power.

- It’s suitable for outdoor use.

- Never use projector without protective glass shield. If it’s broken, please replace it immediately.

- Mount the floodlight in a position that gives the following clearances from adjacent surface:

-above the floodlight---0.5m,

--either side of the floodlight---0.3m

---in front of the floodlight---1.0m

- Please use proper wire for connection.

- Be sure to connect the ground lead.

- Please use double-pole switch.

- The range of fixture’s installation height could be 15M, below 10M by ordinary.

- The fixture’s max. projective area: 0.067m2

- If the lamps do not provide the flexible cable or cord, should be recommended to use at least 60245IEC57 type, cross-sectional area of 1.0MM2 cord.