RECHARGEABLE FLOODLIGHT USER MANUAL

----------Charger

---------------Car Charger(Optional)

- Handle

- Power switch

- Charging socket

SPECIFICATION:

Model:

Voltage: 180-240V/50-60Hz

Degree of protection: IP65

Class of protection: III

Material: Aluminium die-casting

Colour temperature: 6000K

Luminous output: 2200lm

Beam angle: 120 degree

Running time: 2.5-3 hours

Charging time: 5-6hours

NOTE:

LED indicator

Charging: indicator LED keeps red

Full charged: Indicator LED turns to green

All the lamps are 20% charged before delivery

Please use the charger equipped with the lamp.

Please do not turn on the light when charging.

Please do not use a modified or damaged charger.

Please do not leave the lamp in charge over 24 hours.

Please do not disassemble the lamp.

Please recharge the lamp every six months when in stock.

WARNING:

This device utilizes a rechargeable Lithium-ion battery that can rupture, ignite and cause serious injury if being used improperly.

DO NOT place batteries and devices in the fire or high temperature

DO NOT tamper with battery wiring.

DO NOT puncture or damage the batteries.

DO NOT use the batteries that appear damaged.

DO NOT immerse or expose the batteries to the water.

DO NOT alter or modify the batteries.

DO NOT attempt changing the batteries in any manner other than that prescribed in this manual.

DO NOT dispose of the battery in the fire or water.

Fail to heed these warning may result in personal injury or property damage.